## Slide 1
Hospital Pyrolysis System
Mass Balance Model Overview

## Slide 2
Overall Plant Structure
1. Feed System
Mulberry wood chips + water + treatment chemicals
2. Inert Gas System
Carrier gas for pyrolysis process
3. Pyrolyzer (300°C)
Thermal decomposition into char, bio-gas, and bio-oil
4. Char Separator
Separates solid char from gas streams
5. Semi-Batched Fluidized Bed Reactor
Activated char filter for grey water treatment
6. Buffer Tank
Grey water collection and distribution prior to PBR

## Slide 3
Process Flow Diagram
Pyrolyzer
Char Seperator
Fluidized Bed
Wood Chips
Inert Gas
Inert Gas
Gas Mixture
Filtered Water
Char
Used Char
Grey Water

## Slide 4
Mass Balance Tool Architecture
MATLAB System Composer
• Hospital_Context.slx - Visual system architecture
• M_* stereotypes track mass balance properties
MATLAB Scripts
• MassBalanceMaster.m - Complete workflow orchestrator
• VariableList.m - User input variables
• ExportToMaple.m - Export to Maple format
• LoadMapleValues.m - Import calculated values
Maple Environment
• MassBalanceVariables.mpl - Auto-generated variables
• MassBalanceCalculation.mw - User equations
• ExportMapleToMatlab.mpl - Export results to MATLAB
Output
• MapleExportedVariables.m - Calculated results
• Updated System Composer model with solved values

## Slide 5
File Interaction Workflow
Step 1: Initialize
VariableList.m → Hospital_Context.slx
Step 2: Clear Model
Clear all M_* properties in connectors
Step 3: Write Initial Values
Write user variables into model
Step 4: Export to Maple
ExportToMaple.m → MassBalanceVariables.mpl
Step 5: Calculate
Maple solves equations in MassBalanceCalculation.mw
Step 6: Export Results
ExportMapleToMatlab.mpl → MapleExportedVariables.m
Step 7: Import Results
LoadMapleValues.m reads calculated values
Step 8: Update Model
Write calculated values back to Hospital_Context.slx

## Slide 6
Stream [16]: Feed Input to Pyrolyzer
Stream Properties:
Total Mass Flow Rate: 1.5385 kg/s
Chip Mass Flow Rate: 1.0 kg/s (65%)
Water (H2O): 0.3077 kg/s (20%)
Treatment Chemicals: 0.2308 kg/s (15%)
Component Mass Fractions:
  • Chips: 65%
  • Water: 20%
  • Treatment Chemicals: 15%

## Slide 7
Stream [14]: Inert Gas Supply
Stream Properties:
Total Mass Flow Rate: 0.5 kg/s
Inert Mass Flow Rate: 0.5 kg/s (100%)
Purpose:

## Slide 8
Stream [13]: Pyrolyzer Output
Operating Conditions:
Temperature: 300°C | Density: 200 kg/m³
Stream Composition:
Total Mass Flow Rate: 2.0385 kg/s
Char: 0.45 kg/s (22.08%)
Bio-gas (Gas1): 0.25 kg/s (12.26%)
Bio-gas (Gas2): 0.20 kg/s (9.81%)
Water (H2O): 0.3077 kg/s (15.09%)
Treatment Chemicals: 0.2308 kg/s (11.32%)
Inert Gas: 0.5 kg/s (24.53%)
Conversion Fractions (from chips):
  • Char: 45%
  • Gas1: 25%
  • Gas2: 20%

## Slide 9
Stream [5]: Char Separator - Char Output
Stream Properties:
Total Mass Flow Rate: 0.4500 kg/s
Char Mass Flow Rate: 0.45 kg/s
Water (H2O): 4.5×10⁻⁹ kg/s (trace)
Purity:
  • Char Mass Fraction: ~100% (0.99999999)
  • Water Mass Fraction: ~0% (1×10⁻⁸)
Notes:
  Char is extremely dry, suitable for use in PBR filter
  Water content minimized to near-zero through separation

## Slide 10
Stream [6]: Char Separator - Gas Output
Operating Conditions:
Temperature: 290°C | Density: 180 kg/m³
Stream Composition:
Total Mass Flow Rate: 1.5885 kg/s
Volume Flow Rate: 0.008825 m³/s
Bio-gas (Gas1): 0.25 kg/s (15.74%)
Bio-gas (Gas2): 0.20 kg/s (12.59%)
Water (H2O): 0.3077 kg/s (19.37%)
Treatment Chemicals: 0.2308 kg/s (14.53%)
Inert Gas: 0.5 kg/s (31.48%)

## Slide 11
Stream [4]: PBR Filter Output
Stream Properties:
Total Mass Flow Rate: 0.4683 kg/s
Component Breakdown:
  • Char: 0.45 kg/s (96.1%)
  • Water (H2O): 0.01405 kg/s (3.0%)
  • CHx (Contaminants): 0.004214 kg/s (0.9%)
Mass Fractions:
  • Char: 0.961
  • Water: 0.03
  • CHx: 0.009

## Slide 12
Streams [1,2,3]: Grey Water Treatment System
Operating Conditions: 10°C, Density: 999.7 kg/m³
Stream [1]: Buffer Tank Input
  Mass Flow Rate: 0.9997 kg/s
  Volume Flow Rate: 1.0 m³/s
  CHx Concentration: 1.0125 mg/L
  Temperature: 10°C
  Density: 999.7 kg/m³
Stream [2]: To PBR Filter
  Mass Flow Rate: 0.9997 kg/s
  Volume Flow Rate: 1.0 m³/s
  CHx Concentration: 1.0125 mg/L
Stream [3]: Filter Outlet (Treated Water)
  Mass Flow Rate: 0.9814 kg/s
  Volume Flow Rate: 0.9859 m³/s
  CHx Concentration: 0.01 mg/L (99% reduction!)
  Water (H2O) Flow: 0.9857 kg/s
  Fluid Density: 999.7 kg/m³

## Slide 13
Overall Mass Balance Summary
System Inputs:
  Feed Stream [16]: 1.5385 kg/s
  Inert Gas [14]: 0.5 kg/s
  Grey Water [1]: 0.9997 kg/s
TOTAL INPUT: 3.0382 kg/s
System Outputs:
  Gas Stream [6]: 1.5885 kg/s
  Spent Char [4]: 0.4683 kg/s
  Treated Water [3]: 0.9814 kg/s
TOTAL OUTPUT: 3.0382 kg/s
✓ Mass Balance Verified: Input = Output

## Slide 14
Key Performance Indicators
Pyrolysis Efficiency
  • Char Yield: 45% (from wood chips)
  • Bio-gas Yield: 45% (Gas1 + Gas2)
  • Operating Temperature: 300°C
Char Separation Performance
  • Char Purity: 99.99999%
  • Moisture Content: <0.000001%
  • Recovery Rate: 100%
Grey Water Treatment
  • CHx Removal: 99.01% (1.0125 → 0.01 mg/L)
  • Water Recovery: 98.17%
  • Char Adsorption Capacity: 0.9% CHx